## Slide 1: Physical Security
For AAM Members
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 2: What is Physical Security
Security is divided into several areas such as physical security, operational security, electronic security, computer security, etc.
Physical Security deals with building hardening, hardware, locks, landscaping, lighting, etc.
Notes: In the notes section, prepare your script that accompanies this slide. NOTE: Do NOT add or use ANY photos or graphics unless they specifically show the condition you are discussing and you own copyright for the photos or artwork. Do not pirate art 0r photos from Google images, etc. Where we use a photo in the template, you may remove them. They are there to show you where graphics can be placed. We prefer that you do not use artwork as we must research copyright on each one that you use. Please tell the Chair if you have appropriate artwork of photos.

## Slide 3: Physical Security Begins With Good Museum Design
Good principles of design include a solid building with defensible space.
Landscaping should be conducive to good security with sight lines and a defined perimeter.
The architect should not design problems into the building that you must live with.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 4: Construction
The building should be Class A construction.
Provisions should be made to prevent intrusion via windows and doors.
  Tempered glass
  Impact resistant window film
  Bars or shutters
  All perimeter glass would benefit from physical protection including skylights, lay lights, doors with glass, etc.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 5: Construction
Walls around collection storage should resist attempts to break through them.
They should slow the spread of fire.
Similarly, walls to spaces like Security Control should be masonry with concrete fill and bullet resistant glass.
The building should be compartmented with secure doors dividing public from non-public spaces.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 6: Construction
Exterior doors should avoid glass when possible.
Doors to storage and high security areas should be at least hollow metal.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 7: Lighting
There should be adequate lighting on the outside of the building. Lighting should be directed upward against the building. It should backlight the building so intruders at night are highlighted as they move between the light source and the building.
Lights should be evenly dispersed with overlapping cones of coverage.
Lights should not blind cameras or patrolling security.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 8: Lighting
Interior lighting should be adequate for patrolling guards to see.
Exterior lighting should be adequate for cameras to function properly.
Notes: In the notes section, prepare your script that accompanies this slide.

## Slide 9: Fencing and Gates
Exterior fencing on the grounds should not facilitate climbing over. Some fences are little more than an inconvenience because they are easy to use as a ladder.
Gates locked with padlocks require quality padlocks. It is relatively easy to get keys for most consumer padlocks.

## Slide 10: Door Hardware
Quality locks should be used in the museum.
The keyway should be proprietary.
  A proprietary keyway is one whose design is unique and patented. The grooves that enable the key to slide into the lock are milled patented specifications. Key blanks are not commercially available. Keys can’t be copied at local retail stores or locksmiths. Only certain locksmiths will make keys then only with your approval.
Notes: In the notes section, prepare your script that accompanies this slide. Add as many slides as you need. Limit your presentation to those required in a 20 minute program or less. Use this theme only so all presentations match in appearance.

## Slide 11: Exterior Doors Should Not Have a Keyhole
If the building is not occupied at night then one lock with a keyhole is needed to allow employees to come and go.
If the building is secured by a guard at night, no one needs to use the key to get in. The guard inside can let others in who need access.

## Slide 12: Hinges
Doors need quality hinges. It should not be possible to remove the pin in the hinge and remove the door.
Pinned hinges should be used.
  Pinned hinges have set screws or other means of preventing removal of the hinge pin.

## Slide 13: Deadbolts
Collection storage rooms with a single door need a single cylinder deadbolt in addition to any card reader or other lock.
Collection storage rooms with a double door need a drop bolt lock.
  A drop bolt lock will remain locked even if the inactive door leaf is not properly secured by the carriage bolt.

## Slide 14: Deadbolts
Some deadbolts require a key on both sides (double cylinder) and some require a key on the outside and have a thumb turn on the inside (single cylinder deadbolt with thumb turn).
Never use a single cylinder deadbolt with thumb turn lock on a door with glass in it.
All you need to do to get in is break the glass, reach in, turn the thumb turn, and open the door.

## Slide 15: Windows
Consider impact resistant film
  Impact resistant film is the same film that museums use to filter harmful UV rays.
  Too often this is purchased with UV filtering capabilities when it can also be ordered for slightly more money to strengthen the glass.

## Slide 16: Air Vents/Roof Vents
There are many possible penetrations via the roof including through air vents. It is wise to secure these with bars but this is not always possible. It is also good to alarm the vents but this also isn’t practical or possible. So the alternate solution is to saturate the galleries with motion detection.

## Slide 17: Collection Storage Rooms
Bars are often used to secure access via vents.
All doors require high security mechanical locks in addition to any electronic lock.
Doors should not have windows and there should be no windows into collection storage.
Water pipes and drains should be routed around collection storage.

## Slide 18: Small Items In Storage Should be Compartmented
Safes and vaults are required within storage rooms for gold and other high risk small items.
Storage cabinets should be used for larger items.
Cabinets should be lockable.

## Slide 19: Galleries
Ideally, galleries should be able to be locked off during installation.
Galleries should have doors between adjacent galleries to slow thieves and the spread of a fire.
Fire exit doors out of galleries should be equipped with alarmed delay locking hardware where codes permit.
  These are panic bars that do not open the door immediately. They delay 30 seconds before opening unless there is a fire alarm.

## Slide 20: Keys
Key blanks, original keys from which copies are made and spare copies must be locked in a safe or electronic key cabinet. Too often they are hanging on hooks behind a door in a staff room.
Keys to exhibit cases must also be secured.

## Slide 21: What Else?
Physical security is a broad subject and there is often no one right way to achieve many of the objectives.

## Slide 22: Plan “B”
What does a museum do when they can’t implement the optimum solution?
  Sometimes they just can’t afford the best solution.
  Sometimes issues like historic fabric prevent solutions like adding modern locks to historic doors, etc.
  Then what?

## Slide 23: Plan “B”
A good alarm system can compensate for many other problems.
  Example: You are unable to make window glass unbreakable so you install extra motion detection.
  Similarly: You are unable to put bars on air ducts that penetrate the roof so you saturate the galleries with detection.
  Simply do your best.

## Slide 24: Credits
This module prepared by Steve Keller, CPP.
Copyright by the MASC. All Rights Reserved. May not be used for commercial purposes or part of any “for fee” training program