## Slide 1: Security for Off-Site Museum Storage
For AAM Members

## Slide 2: Off-Site Storage
How Secure is Your Collection?

## Slide 3: About This Program
This program is directed to the museums that store collections off site using commercial storage firms. It is also directed to museums considering building their own off site collection storage facilities.
While this standard applies only to commercial off site storage facilities, it serves as an excellent guide for museums building their own facilities.

## Slide 4: What Are the Characteristics of Good Off-Site Museum Storage?
The commercial museum shippers and storage firms have undertaken a project to develop standards for security of items in their care.
Project has been a collaborative effort involving many people.
Museums already have a set of de facto standards but off-site storage is not included.
The objective is to write a document that becomes part of the larger body of security de facto standards.

## Slide 5: What’s Included in the Draft Standard?
Requirements for the building
  Location, construction, etc.
Requirements for security systems
  UL listings; alarm, access control, CCTV, etc
Requirements for Security procedures
  policies must be formal and in writing

## Slide 6: Typical Building Requirements
Class 1A Fire Rating
Acceptable proximity to emergency responders
Adequate water supply for firefighting
Fire separations specified between buildings and mixed uses of space
Adequate on-going building maintenance for systems
Crime statistics in area must be known and available for client inspection—Conduct a CAP Index.

## Slide 7: CAP Index
www.CAPIndex.com

## Slide 8: What Does it Do for You?
CAP Index is a valuable property management tool. It analyzes crime statistics and compares them to surrounding areas. It predicts the likelihood of crimes of various types occurring at any given address in North America.
It indicates whether crime is increasing or decreasing at any given location.

## Slide 9: CAP Proximity Analysis
AIRPORTS, CHEMICAL PLANTS, DAMS, NUCLEAR PLANTS, MILITARY BASE, ETC

## Slide 10: Physical Security Requirements
Bars, shutters or alarms on windows
Roof penetrations addressed
Lock and key requirements addressed
Building lighting defined for exteriors
Loading dock requirements addressed
Elevators addressed

## Slide 11: Safety issues addressed
Location directly on flight path prohibited
Location in flood plain addressed
Safety of electrical systems and temporary lighting addressed
Building perimeters addressed
Alarm system UL Standard compliance addressed
CCTV systems recommended

## Slide 12: Standard vs. High Security
Two levels of security defined for commercial storage facilities
  Standard Level: Collection can be mixed in common storage; General building alarm system protects all; storage facility staff have normal access.
  Gold Seal Level (High Security): Customer can store collections in space which he locks and which is protected by his alarm system; card reader on door; storage facility staff does not have routine access.

## Slide 13: Museum Owned Storage
If this standard were to be applied to museum owned off site storage, the Gold Seal (High) security level would apply.

## Slide 14: Access Control System Addressed--Gold Seal Level of Security
To achieve Gold Seal Level, a Card Access system is required, or
Electronic locks controlled by the guard in a secure control room, or
Two high security locks--one under control of warehouse security manager and one under control of Collection Manager.

## Slide 15: Alarm System Addressed
Generally, alarm requirements are the same as defined in the industry-wide standard for all museums, Suggested Guidelines for Museum Security.
  UL Extent of Protection Level 2 is required for Gold Seal (high security) certification.
  UL Extent of Protection Level 4 is required for all other areas.
  An alarm policy must be provided in writing in detail.

## Slide 16: Dedicated Use--Gold Seal
In gold seal areas, the museum client has exclusive use of a secure access controlled space.
Upgraded construction and wall strength defined.
Door strength defined.
Rapid entry into space in an emergency defined.

## Slide 17: Other Provisions--General
There must be a trained security force on site.
Alarm system must be monitored from a high security control room.
A high security phone line or radio link between the alarm system and UL listed off-site central station for monitoring is defined.
Every aspect of the guard program, alarm and electronic security program and procedures must be clearly defined in a comprehensive policy manual available for inspection of the client and insurer.

## Slide 18: Other Provisions--General
Many policies and procedures are defined.
Proximity to any facility that poses a risk prohibited.
Basements are not suitable for use in storing collections.
Building can’t be located in storm surge tide area.
Construction in hurricane areas is addressed.
May not be located in mixed use facilities that pose a risk to collections--welding, torching, industrial.

## Slide 19: Other Provisions--General
Trees that overhang the building must be trimmed.
Seismic issues addressed to prevent toppling.
Parking directly adjacent to the building addressed.
One section addresses fire prevention issues.
Building inspections by management addressed.
Daily test of alarm system mandated.
Section addresses protection from water risks.

## Slide 20: Other Provisions--General
Access controls defined
Visitor control defined/photo ID must be examined
internal security/employee background checks defined
Visitor escorts defined
Two sections address lock, key and retrieval issues
Parcel control mandated
Section addresses CCTV and where cameras are required.

## Slide 21: Other Provisions--General
Requirements for guards, security managers and guard training defined.
Guard equipment to be used is defined; radios, etc.
Guard breaks and relief periods.
Guard deployment addressed.
Guard patrols defined.
When 24-hr. guard presence is required is addressed.
Protection against environmental risks addressed.

## Slide 22: Other Provisions--General
Disaster plan and supplies required.
Requirements for emergency systems addressed.
Protection against physical damage to objects in transit within the building is addressed.

## Slide 23: Conclusion
This document, when completed and implemented, will improve the level of security for items stored off site by contractors by many orders of magnitude.
Many of the problems we have seen recently--fires due to mixed use of space, destruction due to facilities located in surge tide areas, and thefts--will be eliminated with many other risks reduced.
This document, whether we like it or not, could become the de facto standard that defines the level of security used by museums for their in-house off-site storage facilities and is therefore a valuable tools for us today.

## Slide 24: Courtesy of Steve Keller
Steve Keller is a museum security consultant who worked with a group from the collection storage industry to help develop this document.
The draft standard in its most current form can be found on the www.securitycommittee.org website.